## Slide 1
Jeonghyun Woo, Gururaj Saileshwar*, Prashant Nair
Scalable and Secure Row-Swap: Efficient and Safe Row Hammer Mitigation in Memory Systems
*

## Slide 2: Row Hammer
Aggressor Row
Victim Row
Victim Row
ACCESS (ACTIVATE)

## Slide 3: Row Hammer Attacks

## Slide 4: Row Hammer is Getting Worse
Row Hammer Threshold: Min. Activations for Bit Flips
Chart: 
| DDR3-Old | DDR3-New | DDR4-Old | DDR4-New | LPDDR4 | DDR5
 | 139 | 22.4 | 17.5 | 10 | 4.8
29X in Threshold
Flipping bits [ISCA’2014]
Revisiting RowHammer [ISCA’2020]
Source

## Slide 5: Victim-Focused Mitigations (VFM)
REFRESH
Bit Flip
0
REFRESH
ACTIVATE
Target Row Refresh [2015]
TWiCe [ISCA’19] Graphene [MICRO’20] and others …

## Slide 6: Half-Double Attack on VFM
Google’s Half-Double Attack: Exploits Mitigative Refresh*
Source*: Half-Double [USENIX SECURITY’2022]
Distance-of-2
Distance-of-2
Mitigation  Break Defense
Bit Flip
0
REFRESH
REFRESH
ACTIVATE

## Slide 7: Randomized Row-Swap [ASPLOS’22]
Swap
ACTIVATE
ACTIVATE
SWAP
SWAP
Spatial correlation
Defend Half-Double
3+ Years of Security
Random Guess
Random Guess
Random Guess
Swap Threshold
Security Performance
Bit Flip
0

## Slide 8: RRS Security Pitfall: Latent Activations
SWAP
Memory Controller
ACTIVATE
ACTIVATE
Swap Buffer
Swap Buffer
Swap
Bit Flip
0
Swap Operation  1 Latent Activation

## Slide 9: RRS Security Pitfall: Latent Activations
UNSWAP
SWAP
SWAP
Swap
Bit Flip
0
ACTIVATE
Unswap-Swap Operation  2 Latent Activations

## Slide 10: Juggernaut Attack
ACTIVATE
ACTIVATE AGGRESSOR
ACTIVATE
Exploit latent activations
1
Swap
Bit Flip
0

## Slide 11: Juggernaut Attack
Exploit latent activations
Random Guess
Random Guess
Random Guess
Break RRS in < 4 hours
Random Guess
Guess Aggressor
2
1
Swap
Bit Flip
0
Please see the paper for a detailed security analysis

## Slide 12: Secure Row-Swap (SRS)
Latent Activations
Unswap
2+ Years of Security
Swap-Only
ACTIVATE
ACTIVATE
ACTIVATE
Swap
Bit Flip
0

## Slide 13
Unswap
…
Latency Spike
Performance Degradation
Secure Row-Swap (SRS)
…
Time
Refresh
Refresh
Randomized Row-Swap (RRS)
Unswap
…
Time
Refresh
Refresh
Secure Row-Swap (SRS)
Swap
Bit Flip
0

## Slide 14: Secure Row-Swap (SRS)
No Performance Overhead
Key Idea: Delay unswaps using two separate tables
Time
Refresh
Epoch 1
Unswap Rows in Epoch 1
Unswap Rows in Epoch 2
Odd Table
Even Table
Refresh
Refresh
Refresh
Refresh
Epoch 2
Epoch 3
Epoch 4
Unswap Rows in Epoch 3
Storing General Mapping
Idle
For Unswap

## Slide 15: Implementation of Secure Row-Swap
Memory Controller
DRAM
Place-Back Buffer
Tracker
ACCESS
Not Swapped
Swapped
UNSWAP
Even
Odd
Row Indirection Table (RIT)
Please see the paper for our detailed implementation

## Slide 16: Insight: Scalable & Secure Mitigation
Chart: Number of Outlier Rows
| 1 | 2 | 3 | 4
Probability | 1 | 0.77339 | 1e-05 | 1.7831e-06
Row Hammer Threshold = 4800 Swap Threshold = 1600
Outlier rows: Bypassing SRS  Cause Bit Flips

## Slide 17: Insight: Scalable & Secure Mitigation
Number of Outlier Rows | Attack Time
1 | 12 Secs
2 | 1.3 Hours
3 | 30.7 Days
4 | 64 Years
Few outliers bypass SRS
Pin these outliers in LLC!
Better Scalability

## Slide 18: Scalable and Secure Row-Swap
.
.
.
Cache Lines
Every 31 days
Swap
0
Bit Flip
Last Level Cache
DRAM
Cache Lines
Cache Lines
Cache Lines
Pinning Region

## Slide 19: Scale-SRS: SRAM Overhead
Memory Controller
Place-Back Buffer
Tracker
Even
Odd
Row Indirection Table (RIT)
Row Hammer Threshold | RRS | Scale-SRS
4800 | 36 KB | 18.7 KB
2400 | 131 KB | 44.4 KB
1200 | 251 KB | 76.9 KB
Overhead Per Bank
3.3X lower SRAM Overhead

## Slide 20: Scale-SRS: Performance
Chart: Normalized Performance
| hmmer | bzip2 | h264 | calculix | gcc | zeusmp | astar | sphinx | mummer | ferret | gobmk | blender_17 | freq | stream | gcc_17 | swapt | black | comm1 | xz_17 | comm2 | omnetpp_17 | fluid | omnetpp | face | mcf | gromacs | comm5 | comm3 | gups | SPEC2K6(29) | SPEC2K17(22) | GAP(6) | COMMERCIAL(5) | PARSEC(7) | BIOBENCH(2) | MIX(6) | ALL-78
RRS | 0.876 | 0.782 | 0.915 | 0.93 | 0.735 | 0.897 | 0.864 | 0.854 | 0.98 | 0.956 | 0.965 | 0.923 | 0.963 | 0.963 | 0.981 | 0.96 | 0.949 | 0.977 | 0.894 | 0.918 | 0.991 | 0.982 | 0.995 | 0.991 | 0.928 | 0.993 | 0.983 | 0.942 | 1 | 0.939 | 0.967 | 1 | 0.964 | 0.966 | 0.977 | 0.977 | 0.96
Scale-SRS | 0.964 | 0.897 | 0.978 | 0.971 | 0.938 | 0.975 | 0.977 | 0.971 | 0.993 | 0.987 | 0.996 | 0.984 | 0.991 | 0.991 | 0.999 | 0.994 | 0.988 | 0.998 | 0.946 | 0.99 | 0.994 | 0.998 | 0.998 | 0.996 | 0.999 | 0.998 | 1.004 | 0.993 | 1 | 0.988 | 0.996 | 1 | 0.997 | 0.992 | 0.994 | 0.995 | 0.993
Row Hammer Threshold: 1200
Less than 1% performance overhead

## Slide 21: Summary
Juggernaut  Breaks Randomized Row-Swap (RRS) in < 4 hours
Secure Row-Swap: Secure against 2+ years of continuous attacks
Scalable & Secure Row-Swap  Scalable and Low-Cost Mitigation

## Slide 22: Thank You!
jhwoo36@ece.ubc.ca
JeonghyunW
jeonghyunwoo0306.github.io

## Slide 23: RRS versus Scale-SRS
RRS
Storage Overhead
Performance Overhead
Security
< 4 hours
Scale-SRS
Storage Overhead
Performance Overhead
Security
5%
250KB SRAM/Bank
< 1%
3.3X lower
2+ Years